## Slide 1: Cold metal and Layout
Mr. Patterson
Construction Tech 1

## Slide 2: Cold metal
What is it?
  Working with metal with out using heat
  Includes:
    Bending, Drilling, taping, cutting, rolling

## Slide 3: II. Identification and Use of Basic Metalworking Tools
Metalworking Tools
  Scratch Awl or Scribe - Hardened steel rod with a sharp point that allows you to make marks on steel.
  Tin Snips -Hand-held pliers-like tool used for cutting sheet metal.
  Hacksaw - A hand-held saw with a replaceable blade. Used for cutting all types of thin metals, round and bar stock, pipes, and tubing.

## Slide 4: Scratch Awl and Tin snips

## Slide 5: Hacksaw

## Slide 6: A. Metalworking Tools
  Drill Press - A mounted drill used for precision drilling of portable objects.
  Cold Chisel - Is used with a hammer and vise to shear the metal

## Slide 7: III. Layout and Transfer
Layout Tools - Both measuring and layout tools require skill in use and care in handling and storage.
  Steel Rule - Used to make linear measurements, check straight lines, and to project straight lines onto metal. Usually marked in units to 1/32”.

## Slide 8: III. Layout and Transfer
  Combination Square - Consists of a steel rule, level, and 90 and 45 degree angles. Used to layout markings on metal.

## Slide 9: III. Layout and Transfer
  Metal Tape - Used to layout dimensions longer than a few feet.

## Slide 10: III. Layout and Transfer
  Prick Punch - Is used to transfer directly from the drawing to the sheet metal by placing the drawing on top of the metal and then tapping the punch with a hammer to mark the metal through the drawing.
  Center Punch - Is used to enlarge a mark for a drill to follow in order to prevent wandering of the drill bit.

## Slide 11: Prick Punch Center Punch

## Slide 12: III. Layout and Transfer
  Soapstone - Is a white, soft, natural element cut to either a rectangular or round shape about 4” long and is used to mark rough measurements on steel.

## Slide 13: III. Layout and Transfer
  Sliding “T” Bevel - Is a transfer tool used to copy different angles from a blueprint or project onto the metal.
  Dividers - Used to transfer a dimension from a rule to the metal. Also used to scratch circles or arcs in the metal.

## Slide 14: Sliding T Bevel Dividers

## Slide 15: III. Layout and Transfer
  Calipers - Used to measure the thickness or diameter of an object.
  Compass - Used to mark circles and arcs on metal. The compass uses a pencil attached to one leg to make the mark.

## Slide 16: B. Measurement

## Slide 17: III. Layout and Transfer
  The first step in correct layout is to measure with exact dimensions the item being copied using a rule, metal tape, dividers, and/or compass.

## Slide 18: III. Layout and Transfer
  The ability to read and measure correctly both whole and fractional dimensions from the rule to work and back to the rule requires concentration and counting accurately along the rule.

## Slide 19: III. Layout and Transfer
  Skill at measuring requires practice. You should be able to measure accurately to the nearest 1/16”.

## Slide 20: C. Project Layout
  Project Layout

## Slide 21: C. Project Layout
  Layout or transfer work is the placement of the measurements and lines on the metal.
  Layout work is done in full scale and allows for saw cuts or kerfs as needed.
  Layout can be done from a drawing or from an actual project being copied.

## Slide 22: C. Project Layout
  Transfer the dimensions from drawing to metal using one of the following methods:
    Attach a drawing (full size) to the metal. Use a scratch awl to make an outline of the project.
    Transfer lines from a drawing to metal using a straight edge and scratch awl or soapstone. Be sure all lines are straight and angles are correct.
    Use templates or cardboard to transfer curves and angles.