## Slide 1: Cold Metal Processes
MR. PATTERSON
CONSTRUCTION TECH 1

## Slide 2: Cold Metal Processes
Breaking- bending or forming a flat shape into a 3 dimensional object.
  2 main forms of breaking metal
    Hand breaking-using specially designed hand tool
    (hand seamer) to bend sheet metal
    Machine Breaking
      Press break
      Box Break
      Pan Break

## Slide 3: Breaking Machines

## Slide 4: Example of Flat shape formed to a 3D shape

## Slide 5: Fastening Metal
Drilling
Tapping
Riveting
Bolting

## Slide 6: Drilling
Drilling Procedure
  Layout the center of the hole to be drilled
  Mark the center with two intersecting lines
  Center punch the intersecting lines

## Slide 7: Drilling
Select the correct drill size from a drill index
Put the drill into the drill chuck and tighten with the chuck key.

## Slide 8: Drilling
Clamp material to the table
Place a drop of cutting fluid on the center punch mark
Turn on drill and begin to drill hole
Be sure to put even pressure on the drill

## Slide 9: Cutting Threads
There are 2 ways to cut threads:
  External Threads (bolt)
    Die-cutting threads on the outside of a piece of rod
  Internal Threads (nut)
    Tap-cutting threads on the inside of a hole

## Slide 10: Tapping Procedure
Layout hole location using “Drilling” procedure
Select required tap size and threads per inch (TPI)
Consult Tap Drill chart for hole size

## Slide 11: Tap Drill Chart
Tap Drill Chart |  |  |  |  |  |  |  | 
NATIONAL COARSE THREAD(NC) |  |  |  |  | National Fine Threads (NF) |  |  | 
Size of Bolt |  | Size of | Threads |  | Size of |  | Size of | Threads
or Screw and |  | Drill | Per |  | Bolt or Screw |  | Drill | Per
Tap |  | to Use | Inch |  | and Tap |  | To Use | Inch
1/4" |  | 13/64" | 20 |  | 1/4" |  | 7/32" | 28
5/16" |  | 1/4" | 18 |  | 5/16" |  | 17/64" | 24
3/8" |  | 5/16" | 16 |  | 3/8" |  | 21/64" | 24
7/16" |  | 23/64" | 14 |  | 7/16" |  | 25/64" | 20
1/2" |  | 27/64" | 13 |  | 1/2" |  | 29/64" | 20
9/16" |  | 31/64" | 12 |  | 9/16" |  | 33/64" | 18
5/8" |  | 17/32" | 11 |  | 5/8" |  | 37/64" | 18
3/4" |  | 21/32" | 10 |  | 3/4" |  | 11/16" | 16
7/8" |  | 49/64" | 9 |  | 7/8" |  | 13/16" | 14
1" |  | 7/8" | 8 |  | 1" |  | 15/16" | 14

## Slide 12: Threads inside and out
3 classifications of threads
  National Fine (UNF)
  National Course (UNC)
  National Pipe Thread (NPT)

## Slide 13
Thread Diameter
  Diameter of the thread measured directly over the threads
Thread Pitch- # of threads per inch

## Slide 14: Threading Tools
Tap
Tap handle
Die
Die Stock

## Slide 15: Threading tools cont.
Cutting Fluid

## Slide 16: Riveting
Used as a semi-permanent form of fasting metal together
Can join dissimilar materials together

## Slide 17: Pop riveting
Used when back side of material can not be reached
Used to connect a blind hole

## Slide 18: Pop riveting procedure
Drill hole to correct size for pop rivet
Slip pop rivet into hole
Making sure it is pushed in all the way up to the flange

## Slide 19: Pop riveting procedure
Place the pop rivet gun over the pointed end of the rivet
To seat the rivet squeeze the two handles together until the rivet center pin breaks off.